## Slide 1: Research Project Presentation Improving Navigation through code-based landscapes
Objective: Misdetection Error Model

## Slide 2: Project Context
Understanding the relationship between landscape and navigation safety
Shaping architecture around robotics
Ensuring localization integrity in regions where GNSS is unavailable
Lidar Localization for periodic reset on IMU
Diagram of State Street Transect
Project Proposal - NRI: FND: The Urban Design and Policy implications of Ubiquitous Robots and Navigation Safety

## Slide 3: Code-based landscape
Association problem
  The right measurement to the right mapped object
  Maximum likelihood and nearest neighbor process create uncertainty
Providing a landmark signature though code-based landscape
Retrieving the localization of the landmark
  ID 107  Landmark (42° N, 88° W)
Basis concept of Code based landmark identification
Project Proposal - NRI: FND: The Urban Design and Policy implications of Ubiquitous Robots and Navigation Safety
Creating IDs from a set of measurements
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
1
1
0
1
0
1
1
1
0
1
0
1
1
1
0
1
1
0
1
1
0
1
ID: 1 1 0 1 0 1 1
ID: 1 0 1 0 1 1 1
ID: 1 0 1 1 1 0 1
107
87
93

## Slide 4: This can get complicated
Numerous sources of Noise
  GNSS
  Lidar
  IMU
Irregularity of landmark placement – spatial and temporal
Misdetection possibilities
  0 to 1: Measuring an inexistant landmark
  1 to 0: Not measuring an existing landmark
A more realistic view of Code based landmark identification
Project Proposal - NRI: FND: The Urban Design and Policy implications of Ubiquitous Robots and Navigation Safety

## Slide 5: Error Correcting Codes A brief Overview
Procedures:
  Detect if and how many errors have occurred
  Pinpoint the location of the error(s)
  Correct the error(s)
  Retrieve the initial message
Hamming (7, 4) Codes:
Message : a b c d - 1 1 0 1
Redundancy bits: x y z - 1 0 0
  x = a ⊕ b ⊕ d
  y = a ⊕ c ⊕ d
  z = b ⊕ c ⊕ d
Codeword = a b c d x y z – 1 1 0 1 1 0 0
Parity check: Adding a 1 if uneven number of bits, else 0
Correction of one bit error by checking redundancy bits

## Slide 6: Bose-Chaudhuri-Hocquenghem Codes
BCH [n, k, d] code
Subclass of cyclic code with multiple errors capability
  Cyclic code for handling sequences of landmarks
  At each step, a single bit changes in the sequence
Choosing the number of errors to correct generates the code
Polynomial representation of a code vector:
Code vector v:
Cyclic nature of the IDs
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
1
1
0
1
0
1
1
1
0
1
0
1
1
1
0
1
1
0
1
1
0
1
ID: 1 1 0 1 0 1 1
ID: 1 0 1 0 1 1 1
ID: 1 0 1 1 1 0 1
107
87
93

## Slide 7: Error Model Probability of misdetection
Focusing on the misdetection
1  0: not detecting an existing landmark
Referred as the transitional probability
p(1  0): probability of not detecting our landmark from the ratio between dimensions of landmark and section of detection
Representation Landmark and Lidar detection
2r
W1
W2
Parameters | Values
σx | 1 cm
σy | 2 cm
Δθ | 0.2 deg
Δσ | 6.6 cm
Δδ | 0.1 deg
d | 6.35 to 10.2 cm

## Slide 8: Sections of bit assignments
Imposing sections of measurements and bit assignement
Unambiguously Identifying and replacing landmarks
To many sections creates lots of zeros
Not enough sections potentially looses information
Measurement Ld vs Truth Ld

## Slide 9: Selected Sections of detection
Imposing step between or sections of measurements
Practical for constructing a code
  Placing a 1 in the section if a landmark is detected
  Placing a 0 if not
Selected sections with a nominal range

## Slide 10: Shape of sections of detections
Proposed Shape:
  Rectangular
  Trapezoid
Construction by edge cases of
  Incertitude of position
    GNSS sigmas
    IMU drift
  Incertitude of lidar
Rectangular and Trapezoid: 1 to 5 meters from sidewalk
Trapezoid Section – 10 cm tree – σ and 3σ

## Slide 11: Ratio and probabilities
σ values for probabilities:
  σ for 67%
  3 σ for 99%
 | σ | 3 σ
L1 = 1m, r = 3 cm | 3.0135 | 0.9905
L1 = 5m, r = 3 cm | 1.1846 | 0.3922
L1 = 1m, r = 5 cm | 4.8405 | 1.5911
L1 = 5m, r = 5 cm | 1.9029 | 0.6300
 | σ | 3 σ
L1 = 1m, r = 3 cm | 3.0135 | 0.9905
L1 = 5m, r = 3 cm | 1.1846 | 0.3922
L1 = 1m, r = 5 cm | 4.8405 | 1.5911
L1 = 5m, r = 5 cm | 1.9029 | 0.6300
 | σ | 3 σ
L1 = 1m, r = 3 cm | 1.9184 | 0.6306
L1 = 5m, r = 3 cm | 0.7542 | 0.2497
L1 = 1m, r = 5 cm | 3.0816 | 1.0129
L1 = 5m, r = 5 cm | 1.2114 | 0.4011
 | σ | 3 σ
L1 = 1m, r = 3 cm | 1.9184 | 0.6306
L1 = 5m, r = 3 cm | 0.7542 | 0.2497
L1 = 1m, r = 5 cm | 3.0816 | 1.0129
L1 = 5m, r = 5 cm | 1.2114 | 0.4011
Ratio for circular curve
Ratio for projected curve
Widths of sections vs distance from sidewalk
 | σ | 3 σ
w1 for L1 = 1m | 0.0331 m | 0.1007
w1 for L1 = 5m | 0.0842 m | 0.2543

## Slide 12: Conclusion and Perspective
Defining the error model to take incertitude of IMU drift into account
Adding noisy landmark and test the process with BCH encoding –decoding